## Slide 1: EMBEDDED SYSTEMS LAB3 FPGAS AS ACCELERATORS
Ioannis Papadopoulos, Maria Ilektra Tzormpatzaki
Student IDs: 03899, 03993

## Slide 2: Software (x86 CPU)

## Slide 3: LSAL Implementation on the x86 CPU
Nested loop structure
  Outer loop length of the database M
  Inner loop length of the query N
Find the highest score from: North-West, North, and West.
Store the result in Similarity and Direction Matrix.

## Slide 4: Picking the best implementation (1)
Inputs | lsal | lsal_plus1
N=32 M=65536 | 0.016693 | 0.015844
N=256 M=65536 | 0.130641 | 0.120686
N=256 M=300000 | 0.570392 | 0.557866
north = (j > 0) ? similarity_matrix[index- N] : 0;
west = (i > 0) ? similarity_matrix[index- 1] : 0;
northwest = (i > 0 && j > 0) ? similarity_matrix[index- N- 1] : 0;
north = similarity_matrix[index - N - 1];
west = similarity_matrix[index - 1];
northwest = similarity_matrix[index - N - 2];
Padding
non-Padding

## Slide 5: Picking the best implementation (2)
Inputs | lsal_plus1 | lsal_outside
N=32 M=65536 | 0.015844 | 0.014536
N=256 M=65536 | 0.120686 | 0.117629
N=256 M=300000 | 0.557866 | 0.538566
for (j = 0; j < M; j++) {
string2_temp = string2[j];
row_offset = j * N;
for (i = 0; i < N; i++) {
index = row_offset + i;
...
match_score = (string1[i] == string2_temp) ? MATCH : MISS_MATCH;
}
}
Outside

## Slide 6: Software (Arm CPU)

## Slide 7
Chart: Input Sizes (N,M)
| N=32, M=65536 | N=256, M=65536 | N=256, M=300000
x86 | 0.014536 | 0.11763 | 0.53857
ARM | 0.0727 | 0.5609 | 2.528
Chart: Input Sizes (N,M)
| N=256, M=65K | N=256, M=300K
Arm / x86 Ratio | 5 | 4.77 | 4.69
The Arm Cortex-A9 is slower
  lower clock frequency
  smaller cache hierarchy
  lack of out-of-order execution
Hitting the Memory Wall
  Both CPUs are memory-bound, narrowing the gap

## Slide 8: Hardware (FPGA)

## Slide 9: Step 1: Serial logic
AXI Interface Mapping
Local Buffering
  local_string1
  local_west
  local_northwest
  prev_row
  local_dir_row
Burst Writes: Writing the results back to external memory row-by-row .
Pipelining query and internal loop.
Metric | Result
Total Time (ms) | 254.111
CU Total Time (ms) | 178.206
LUT | 4,089 (7.69%)
Registers | 6,182 (N/A)
BRAM | 6 (4.29%)

## Slide 10: Step 2
Anti-Diagonal Execution (Computing up to 32 cells concurrently.)
Local Database Fetching (local_string2):
  Pre-loading 32 database characters before the internal loop begins.
Complete Array Partitioning:
  3 diagonal buffers.
  local strings and local direction buffer.
If-else structure for Priority Encoder:
  Moved the global maximum tracking on the outside loop.
Metric | Result
Total Time (ms) | 99.573
CU Total Time (ms) | 69.359
LUT | 14,572 (27.39%)
Registers | 15,537 (N/A)
BRAM | 21 (15.0%)

## Slide 11: Step 3
Arbitrary Types
  3bit Query and Database
  512bit wide word of 32 packed outputs
Shift-Register Window (local_string2_window)
5-Level Parallel Reduction Tree:
  Finds the maximum in just 5 combinational steps (log2(32) = 5) instead of 32.
Metric | Result
Total Time (ms) | 13.304
CU Total Time (ms) | 8.614
LUT | 11,285 (21.21%)
Registers | 9,556 (N/A)
BRAM | 17 (12.14%)

## Slide 12: Step 4
Elimination of the Similarity Matrix.
Direction Matrix Compression:
  2bit directions instead of 16bits.
Metric | Result
Total Time (ms) | 7.722
CU Total Time (ms) | 4.816
LUT | 9,076 (17.06%)
Registers | 5,329 (N/A)
BRAM | 2 (1.43%)

## Slide 13: Step 5
Ultra-Wide Input Fetches (ap_uint<512>):
  Fetching the complete Query at startup.
  Fetching a 512bit block from Database only when needed
Metric | Result
Total Time (ms) | 1.991
CU Total Time (ms) | 0.729
LUT | 10.293 (19.35%)
Registers | 9.313 (N/A)
BRAM | 11 (7.86%)

## Slide 14
Chart: 
| Step 1 | Step 2 | Step 3 | Step 4 | Step5
Total Time (ms) | 254.111 | 99.573 | 13.304 | 7.722 | 1.991
Chart: 
| Step 1 | Step 2 | Step 3 | Step 4 | Step 5
Speedup (x) | 1 | 2.5 | 19.1 | 32.9 | 127.6

## Slide 15
Chart: 
| Step 1 | Step 2 | Step 3 | Step 4 | Step 5
BRAMs | 6 | 21 | 17 | 2 | 11
Chart: 
| Step 1 | Step 2 | Step 3 | Step 4 | Step 5
LUTs | 4089 | 14572 | 11285 | 9076 | 10293
Chart: 
| Step 1 | Step 2 | Step 3 | Step 4 | Step 5
Registers | 6.182 | 15.537 | 9.556 | 5.329 | 9.313

## Slide 16
Chart: 
| N=32, M=65536 | N=32, M=100000 | N=32, M=125000 | N=64, M=65536 | N=64, M=125000
Bigger Inputs (ms) | 1.991 | 2.5 | 2.92 | 29 | 54.7